ID	Functional Safety Requirement	Allocation to Element	ASIL
FSR1	The brake lamps shall be activated within 50ms of receiving a brake signal. * [1, p. 5.2.22.1]	Logic Unit, Brake Pedal, Turn Signal*	D
FSR2	The brake lamps shall be activated if the acceleration of the vehicle is measured to be > 1.3 m/s2 while the vehicle is in regenerative braking (one pedal) mode and shall remain activated until the acceleration is measured to be <= 1.2 m/s2. * [1, p. 5.2.22.2]	Logic Unit, Driving Mode Signal, Turn Signal*	D
FSR3	The brake lamps shall not be activated if a turn signal is active. ** [2, p. 93]	Logic Unit, Turn Signal**	D
FSR4	Faults in the logic unit, which would lead to an unintended activation of brake lamps, shall be detected within 50ms.	Logic Unit	D
FSR5	Faults in the logic unit, which would lead to a failure to illuminate when signaling* or braking, shall be detected within 50ms.	Logic Unit, Brake Pedal, Turn Signal*	D

* In the case that the system is configured for unified brake and rear turn signals, the brake lamps shall only be activated if the turn signal is not active.
** In the case that the system is not configured for unified brake and rear turn signals, this requirement shall not be considered.
# Works Cited